## Slide 1: Deviation Analysis Pipeline

## Slide 2: I. Building the dataset - get_trq_stats()
Gets the mean, standard deviation and quantiles for each operation
Skip HV141 and HV157 because apparently they were run twice – Not sure which values to take
Skip all HV with Störung==1
Preprocessing with utils.read_timeseries_data()
Use the friction model to correct the torque values for each Bezeichnung in [‘Aussenkontur’, ‘Steg’, etc.]:
  Get the operation name
  Get only the period in which the spindle speed is constant and greater than zero using utils.get_operation_interval()
  Filter the data for removed_volume > 0
  Find the most common tool for the relevant operation and filter for that
    This is necessary because sometimes the operation name in the dataset changes before the tool is changed, so, in the first moments of an operation, the machine might have the wrong tool
    However, as we have already filtered for constant and maximum spindle speed, the tool should be correct already. So this step is just for precaution
  Get torque stats for this preprocessed df

## Slide 3: II. Building the dataset – build_df_trq_dev()
Merges the quality data with the torque stats obtained with get_trq_stats()
Also calculates the deviation for each Bezeichnung based on a dictionary of expected values for each measure, e.g.
EXPECTED_VALUES = {
'Aussenkontur': {'columns': ['XMaß_Zmax [mm]', 'YMaß_Zmax [mm]'], 'expected_values': [60, 60]}
}
Saves the final dataframes both as .csv (one file per Bezeichnung) and .xlsx (one single file, with one sheet per Bezeichnung)

## Slide 4: utils.read_timeseries_data()
Reads and merges all timeseries datasets (from one single HV) necessary for the deviation pipeline
  drive, prog, cnc, tool and simulation data
  As this data is not available for some HV, the function returns an empty DF if pd.read_csv() fails
All DFs are merged using pd.merge_asof(direction=‘backward’), i.e. forward fill
  Only the relevant columns are merged into the final DF
‘S1ActTrq’ is converted to N.m
‘S1Actrev’ is converted to RPM
Returns the merged DF with all timeseries data

## Slide 5: utils.get_operation_interval()
For a given timeseries df and operation name, returns only the period in this df in which the spindle speed is constant and greater than a given minimum
Find all continuous time intervals in which the spindle speed is greater than the minimum, for the given operation
  If more than 1 interval is found, something is wrong
Within the period of spindle speed > minimum, find all continuous time intervals in which the spindle speed is within [S1Actrev.max() -1, S1Actrev.max()]
  If more than 1 interval is found, something is wrong